## Slide 1
INDUSTRIAL DEFECT DETECTION SYSTEM
Real-Time Edge AI Computer Vision & Automated PLC Sorting Pipeline
Production-Ready Architecture for Steel Strip Surface Defect Quality Control
Core Technologies
• Framework: FastAPI & Python 3.13
• Inference Engine: ONNX Runtime (CPU/CUDA)
• Model: Improved YOLOv8s (71.0% mAP50)
Edge Capabilities
• Latency: ~8.1ms GPU (123 FPS)
• Industrial Protocol: WebSocket PLC Telemetry
• Monitoring: Prometheus & Glassmorphic UI
Deployment
• Containerization: Docker & Docker Compose
• CI/CD: Automated GitHub Actions
• Test Coverage: 33/33 Pytest Suite Passed

## Slide 2
INDUSTRIAL CHALLENGE
Manufacturing Context & Problem Statement
Overcoming limitations of traditional manual inspection in high-speed rolling mills
Traditional Inspection Pitfalls
• High Line Speeds: Steel strip lines run at >10 m/s, making manual human inspection physically impossible and prone to eye-fatigue error.
• Micro-Scale Defects: Defects like crazing and fine scratches exhibit low contrast against raw metallic sheen, escaping human sight.
• Expensive Scrap Losses: Uncaught defects travel downstream, turning entire coils into scrap or causing catastrophic mechanical failures in client dies.
• Lack of Traceability: Traditional lines lack automated timestamped coordinate logs and real-time defect telemetry for audit compliance.
Our Edge AI Solution
• Sub-10ms Real-Time Inference: Hardware-accelerated ONNX engine delivers real-time defect isolation (~8.1ms / 123 FPS) on edge GPUs.
• Per-Class Optimized Thresholds: Custom F1-calibrated confidence tuning prevents false-positives while guaranteeing 67.9% global recall.
• Simulated PLC Synchronization: Instantly emits WebSocket JSON coordinate payloads to trigger robotic sorting mechanisms and reject gates.
• Full-Stack Observability: Prometheus scrape endpoint and glassmorphic telemetry dashboard provide continuous line visibility.

## Slide 3
DEFECT CLASSES
NEU Metal Surface Defect Taxonomy
Comprehensive detection across 6 critical hot-rolled steel surface flaws
Patches (92.1% AP50)
• Thick, high-contrast surface irregularities. +4.0% gain over baseline. High precision & clear boundary delineation.
Inclusion (76.1% AP50)
• Non-metallic particles trapped inside metal matrix. Recall: 76.1%. Granular multi-point clusters.
Pitted Surface (82.1% AP50)
• Localized pitting/cavities from acid pickling. +5.8% gain over baseline. Distributed pinhole craters.
Scratches (73.1% AP50)
• Linear mechanical abrasions from rollers. High 80.2% recall across long diagonal thin trails.
Rolled-in Scale (53.1% AP50)
• Iron oxide scales pressed during rolling. Irregular dark textured patches.
Crazing (49.6% AP50)
• Network of spiderweb micro-cracks. +6.2% improvement over baseline with multi-scale feature pyramids.

## Slide 4
PIPELINE DESIGN
End-to-End System Architecture
Data flow from camera ingest to edge inference, visualization, and PLC automation
1. Ingestion Layer
• Multi-Source Ingestion: Ingests live USB/IP industrial camera, local MP4 video file, or looping validation directory.
• VideoStreamProcessor: Decodes frames, maintains state, handles auto-reconnect and resolution normalization.
• Dynamic Switching: Enables runtime switching between sources via REST API without server restart.
2. AI Inference Engine
• ONNX Runtime Core: Hardware-accelerated engine supporting TensorRT, CUDA, and OpenVINO/CPU.
• Letterbox Preprocessing: Preserves aspect ratio with symmetric zero-padding and normalized float32 tensors.
• End-to-End NMS ONNX: Embedded Non-Maximum Suppression with per-class F1-calibrated confidence thresholds.
3. Actuation & UI Layer
• MJPEG Video Stream: Multipart live annotated video stream with bounding boxes and latency telemetry.
• WebSocket PLC Broadcast: Coordinates dispatched to sorting actuators within milliseconds of detection.
• Prometheus Metrics: Counters and Gauges exported at /metrics for Grafana / line monitoring.

## Slide 5
MODEL OPTIMIZATION
Improved YOLOv8s & Hardware-Accelerated ONNX
Ultra-low latency execution on edge computing nodes
GPU LATENCY
8.1 ms
RTX 2050 (123 FPS)
GLOBAL RECALL
67.9%
+4.8% vs Baseline
WEAKEST CLASS
+6.2%
Crazing AP50 Jump
GLOBAL MAP@50
71.0%
Peak 71.5% mAP50
Why ONNX Runtime over Raw PyTorch?
• Zero Python Overhead: Optimized C++ execution graph eliminates GIL bottleneck and PyTorch tensor overhead.
• Cross-Hardware Portability: Seamlessly targets x86 edge servers, NVIDIA Jetson, or ARM industrial gateways without code modification.
• Operator Fusion & Constant Folding: Pre-computes graph constants and fuses Conv+BatchNorm+SiLU kernels for peak memory bandwidth efficiency.
Letterbox Preprocessing Architecture
• Aspect Ratio Preservation: Calculates exact scaling factor and applies minimum padding to 640x640 input grid.
• Inverse Coordinate Mapping: Maps bounding box predictions back to original raw image resolution seamlessly.
• Vectorized Array Operations: Fully implemented in NumPy/OpenCV for sub-millisecond preprocessing latency (~1.8ms).

## Slide 6
PRECISION ENGINEERING
Dynamic Class-Specific Confidence Thresholds
Balancing Precision vs Recall based on defect severity and visual distinctiveness
The Problem with Global Thresholds
• Unequal Defect Saliency: A global threshold of 0.50 catches Patches (88.1% AP) perfectly, but drops recall on Crazing (43.3% AP) down to 20%.
• Safety vs False Alarm Tradeoff: Critical safety flaws (Crazing, Scratches) require maximum recall to prevent catastrophic failures.
• Visual Granularity Disparity: Inclusions and Pitted surfaces produce smaller bounding boxes compared to broad roll patches.
• F1-Score Empirical Tuning: Thresholds were mathematically tuned on 360 validation images to maximize F1-score per class.
Optimized Threshold Configuration
• Patches -> 0.50: High visual contrast allows strict thresholding with 91.2% precision.
• Inclusion -> 0.39: Optimized to isolate small particle clusters from background grain.
• Pitted Surface -> 0.30: Filters out lighting reflections while catching surface pinholes.
• Rolled-in Scale -> 0.25: Prevents texture confusion with unrolled metal substrate.
• Crazing -> 0.23: Boosts recall for spiderweb cracks blending into metal sheen.
• Scratches -> 0.22: Maintains detection across faint, low-contrast linear scratch lines.

## Slide 7
OPERATOR INTERFACE
Glassmorphic Web UI & Live Telemetry
Modern, operator-focused monitoring dashboard built with FastAPI & Chart.js
1. Live Video Stream
• Multipart MJPEG: Delivers smooth video streaming at 30+ FPS directly into the browser without plugins.
• Real-Time Overlay: Dynamic bounding boxes, class labels, confidence scores, and per-frame latency badges.
• Source Control: Webcam, directory loop, video file, or instant file drag-and-drop upload.
2. Real-Time Telemetry
• Chart.js Time-Series: Visualizes real-time FPS and latency fluctuations over sliding time windows.
• Defect Class Distribution: Live doughnut chart updating defect frequencies by category.
• Status Badges: Instant system health, camera uptime, and active connection counter.
3. Quality Audit Logs
• Inspection Event Table: Timestamped event stream recording every detected defect coordinate.
• JSON Audit Export: One-click /api/export_report for ISO quality management and shift reports.
• REST Detection Sandbox: Interactive single-image upload with bounding box visualization.

## Slide 8
INDUSTRIAL AUTOMATION
Simulated PLC Actuation & Sorting Protocol
Zero-latency synchronization with Programmable Logic Controllers (PLCs)
WebSocket PLC Broadcast Protocol
• Event-Driven Dispatch: Whenever a defect is confirmed by the ONNX detector, a structured JSON payload is broadcast to all active PLC endpoints.
• Thread-Safe Async Loop: Background video processing thread dispatches safely into the asyncio event loop via asyncio.run_coroutine_threadsafe.
• Connection Resilience: Automatic cleanup of disconnected clients (_safe_send_ws) prevents memory leaks or stream stalling.
Payload Schema & Sorting Logic
• Coordinate Precision: xmin, ymin, xmax, ymax formatted in both absolute pixels and normalized ratios.
• Confidence & Class ID: Provides actuator with class priority (e.g. Scratches vs Crazing) to trigger differentiated sort bins.
• Timestamp & Frame Index: Precise millisecond timestamps for encoder wheel synchronization along conveyor lines.
• Actuator Triggers: Triggers pneumatic ejector gates, marking sprayers, and alarm beacons.

## Slide 9
QUALITY ASSURANCE
Enterprise DevOps, Testing & Containerization
Built for high reliability, automated verification, and rapid deployment
Docker Containerization
• Multi-Stage Dockerfile: Lightweight Python 3.13 image with minimal OS graphics libraries (libgl1, libglib2.0).
• Docker Compose Stack: Orchestrates the FastAPI service and Prometheus scraper in an isolated network.
• Automated Health Checks: Configured HTTP container health monitoring at /api/health with auto-restart.
Continuous Integration
• GitHub Actions Pipeline: Automated CI runs on every push and PR against main/master branches.
• Automated Test Suite: Executes full test matrix across API routes, ONNX inference, and video stream processors.
• Zero Dependency Drift: Explicit requirements lock ensuring reproducible builds on any environment.
100% Test Pass Rate
• 33 Automated Tests: Comprehensive pytest coverage across 4 dedicated test modules.
• tests/test_api.py: 14 tests verifying all REST endpoints, form uploads, and JSON contracts.
• tests/test_onnx_inference.py: 10 tests validating tensor math, NMS, and class metadata.
• tests/test_video_stream.py: 4 tests checking directory loops, overlays, and camera failover.

## Slide 10
CONTINUOUS IMPROVEMENT
Error Analysis & Technology Roadmap
Documented failure modes, mitigation strategies, and next-phase innovations
Failure Mode Analysis & Mitigation
• Crazing Micro-Cracks: Downsampling to 640x640 reduces gradient visibility. Mitigation: CLAHE contrast enhancement & lowered 0.23 threshold.
• Rolled-in Scale Granularity: Texture overlap with base steel grain. Mitigation: Albumentations RandomBrightnessContrast and ISONoise training pipeline.
• Diagonal Scratches: Fragmented bounding boxes on long diagonal abrasions. Mitigation: IoU NMS tuning (0.45) and rotation augmentations.
Future Roadmap
• FP16 / INT8 TensorRT Quantization: Targeting ~2.2ms latency for high-speed lines (>25 m/s) on NVIDIA Jetson Orin.
• OPC-UA / MQTT Industrial Protocols: Native integration with Siemens S7, Rockwell Allen-Bradley, and Beckhoff PLCs.
• Multi-Camera Multi-View Sync: Simultaneous top-and-bottom surface inspection using dual asynchronous ONNX streams.
• Active Learning Feedback Loop: One-click operator flagging of false-positives for automated retraining.

## Slide 11
EVALUATION SUMMARY
Project Impact & Evaluation Takeaways
High-performance edge solution ready for real-world industrial deployment
Key Achievements
• Real-Time Edge Speed: Surface defect detection operating at ~8.1ms / 123+ FPS GPU real-time throughput.
• 71.0% Global mAP50: Enhanced accuracy (peak 71.5%) with 67.9% recall (+4.8% gain) on the NEU-DET benchmark.
• F1-Optimized Tuning: Class-specific confidence thresholds maximizing safety-critical defect recall.
• Zero-Downtime Multi-Source: Seamless runtime switching between live webcam, validation loop, and video files.
• Industry 4.0 Ready: WebSocket PLC triggers, Prometheus metrics, and full Docker orchestration.
Evaluator Quick-Start
• 1-Command Docker Deployment: docker compose up --build (Spins up FastAPI at :8000 and Prometheus at :9090).
• Live Interactive Dashboard: Open http://localhost:8000 to interact with the real-time detection UI.
• Interactive OpenAPI Swagger: Visit http://localhost:8000/docs to test all REST endpoints directly.
• 100% Passing Test Suite: Run py -3.13 -m pytest tests/ -v for automated verification of all 33 tests.